## Slide 1
Deterministic Alarm Correlation
…without the platform tax
Topology-aware root-cause suppression on open-source tooling — Zabbix, Nautobot, a small Python CEP sidecar, Grafana.
A working demo · alternative to the HPE / OpenText TeMIP route
Notes: Frame: this is a capability demo, not an anti-vendor rant. The claim is that the *capability* is commodity; the *price* buys carrier-scale runtime and support.

## Slide 2
The problem a NOC actually has
One fault. Hundreds of alarms. Operators drown in symptoms.
200
raw alarms from ONE upstream failure
Every device behind the fault alarms independently
No way to tell the cause from the consequences
Alert fatigue → real incidents missed
This is the gap TeMIP is sold to close

## Slide 3
What TeMIP sells — and where it's beatable
TeMIP claim | Reality | Open-stack answer
Vendor-neutral normalisation | An inventory + tagging problem | Nautobot is the source of truth
Topology-aware RCA | A Drools rule engine over a topology model (UCA EBC) | networkx graph + windowed rules
Carrier scale (millions/s) | The real reason for the price | Kafka + FlinkCEP/Drools — open source
X.733 lifecycle / state | Mature | Deterministic ROOT/SYMPTOM/CLEARED states

## Slide 4
Architecture
Reuses what you already run; adds one Python container.
Nautobot
topology + dependency (GraphQL)
Zabbix
problems you already collect
CEP sidecar
windowed topology-keyed RCA
Grafana
throughput · latency · ratio
React Flow UI
live correlation visual
Same deterministic rule, three runtimes — pure Python (lab) → +Redis (mid) → Kafka+Flink/Drools (carrier).

## Slide 5
The demo network — 32 nodes
RSTP-protected rings (mstpd) + long routed spurs (FRR/OSPF).
18
RSTP ring switches (3x6)
3
FRR distribution
9
spur routers (chains)
2
redundant cores
Ring members have no RCA parent — RSTP protects them, so a single ring-link break must NOT cascade. The correlator proves that contrast.
Spurs are single-threaded — losing the head cascades down the whole chain, producing the high suppression ratios that sell the story.

## Slide 6
The number that lands
One root cause absorbs the storm — measured live in Grafana.
99.5%
noise reduction
sub-millisecond per alarm · on a laptop
Chart: 
| Before correlation | After correlation
Alarms operators see | 200 | 1

## Slide 7
Same rule, three runtimes
Capability is constant. Only the engine changes with scale.
Lab / regional
Pure Python sidecar
1000s alarms/s · the demo · most real needs
Mid
Python + Redis (N workers)
10k+/s · national network
Carrier
Kafka + FlinkCEP / Drools
millions/s · the only tier that may justify TeMIP — still open source
TeMIP / UCA EBC is literally a Drools rule engine over a topology model. We demonstrate the same architecture.

## Slide 8
Honest caveats
Say these in the room — they build credibility.
TeMIP is mature & carrier-grade
At true telco volumes with strict SLAs and 24/7 vendor support, it earns its place.
This demo's engine is lab-tier
The production equivalent is Kafka + FlinkCEP/Drools — real engineering, not a weekend.
The hard part isn't the engine
It's keeping the dependency graph accurate — a data discipline you need regardless of vendor.

## Slide 9
Recommendation
Adopt the open stack for the regional / mid tier — it covers the majority of real correlation needs.
Reserve a carrier-grade evaluation for the specific contracts that genuinely run at millions-of-alarms scale.
Prove the capability first with this demo. Let the scale requirement — not the vendor pitch — drive any spend.
github.com/mmorrow24work/CEP